Introduction

I have a Master's degree in Geography from the University of Freiburg and a Master's degree in Geoinformatics from the University of Mainz

Projections

We want to display a three-dimensional object (the earth ;-)) in two dimensions (namely on a screen or paper).

There are various approaches to this:

What is the difference between geographic coordinate systems and projected coordinate systems?

Geographical coordinate systems:
Longitude and latitude coordinates
on a sphere / (rotational) ellipsoid

Projected coordinate systems:
Mathematical conversion to convert longitude and latitude coordinates located on the earth's surface into a two-dimensional surface.

The projections should fulfil three requirements:

Longitudinal fidelity (i.e. the measured distance on the map corresponds to the actual distance on earth)
Area fidelity (i.e. the calculated area on the map corresponds to the actual area on the earth)
Angular fidelity (i.e. the measured angles on the map correspond to the actual angles on the earth)
But only the globe fulfils all three criteria at the same time, because with every mapping of the curved surface of the earth onto a flat map, one or two criteria must be neglected, depending on what purpose the map is intended to fulfil. In addition, distortions, i.e. deviations from the true-to-life image, can occur to a greater extent at the edges of the map.
What are projected coordinate systems?

QGIS GUI

directory tree

tabs → vector, raster, processing